## Slide 1: Automated spatiotemporal annotation of sound objects in a scene
Einari VAARAS
Kalle LAHTINEN
Mehmet AYDIN
COMP.SGN.250 Signal Processing Innovation Project
Final Presentation

## Slide 2: Introduction
Audio streams, such as broadcast news, documentaries and personal videos contain sounds from a wide variety of sound sources
These streams include detectable audio events of interest, such as speech, music or sounds of animals
Beside the detection of sound event presence there is a need for detecting the direction of arrival (DOA) of the detected sound event. For such cases Deep Learning methods are often used but requires annotated data which is laborious and difficult to do reliably
The aim is to explore the possibility of automatically annotating spatial and temporal dimensions of sound objects detected in an audio stream with the help of a 360-degree

## Slide 4: Project Steps
Studying object detection methods for 360-degree video data
Determining and defining the scenes to be recorded
Recording spatiotemporal scenes with a 360-degree camera and integrated 360-degree microphone
Applying object detection to the video recording
Extracting temporal object detections and their locations from the video recording
Formulating spatiotemporal labels for the audio data by combining video and audio detections

## Slide 5: Technologies
Ricoh Theta V 360 camera and TA-1 3D microphone module
  Microphone array of 4 microphones
YOLO (You Only Look Once) version 4 video detection network applied on 360 equirectangular video frames
  Method based on paper by Wenyan Yang, Yanlin Qian, Francesco Cricri, Lixin Fan, Joni-Kristian Kamarainen
  Open source github project found to use as a basis
B-format audio decoding, powermap calculation and beamforming scripts provided by Archontis Politis

## Slide 6: Implemented Pipelines
Pipeline version 1
Pipeline version 2

## Slide 7: Pipeline version 1

## Slide 8: Video Detector and Detection Output
YOLO video detection network
Equirectangular video frames projected to 4 sub image planes, which is fed to the detector
  So 4 YOLO detections per 360 frame
  Mp-YOLO –project (by Tsung-Shan, Yang) provided the projection implementation
  We complemented the code to process video files, fixed a minor bug and added the functionality to output detections to a csv-file
Detections in sub images -> Detection coordinates transformed back to equirectangular frame coordinates

## Slide 9: Detection Output
Detections outputted to csv-file (frame id, class id, label, confidence, bounding box center coordinates, bounding box size)
All this is done offline, i.e. no hard time requirements for processing time

## Slide 10: Demo video 1
(video with cell phone)

## Slide 11: Demo video 2
(video with sink)

## Slide 12: Demo video 3
(video with keyboard)

## Slide 13: Clean overlapping bounding boxes
Basic idea of algorithm:
  If there are same classes present in the same video frame:
    If there are overlapping bounding boxes (determined by IoU):
      If overlap exceeds a predetermined threshold:
        Remove bounding box with least confidence

## Slide 14: Demo of cleaning overlapping bounding boxes (initial video)
(video with the three of us talking, no cleaning for bounding boxes)

## Slide 15: Demo of cleaning overlapping bounding boxes (cleaned bounding boxes)
(same video as in previous slide, cleaned bounding boxes)

## Slide 16: Class mapping function
It is possible to change the class indeces and names of classes into arbitrary classes

## Slide 17: Demo of mapping classes
(video with the three of us talking with an arbitrary mapping of classes)

## Slide 18: Audio powermap
A function made by Archontis converts the B-format audio into a powermap
  MUSIC (MUltiple SIgnal Classification) algorithm used

## Slide 19: Demo of audio powermap
(video of audio powermap without any cropping)

## Slide 20: Crop powermap using bounding boxes
The detectected bounding boxes in the frame are used to crop the powermap array
  Values within the bounding box are left unchanged, everything else is set to zero

## Slide 21: Demo of cropped powermap
(video of audio powermap with cropping)

## Slide 22: Determine energy based on cropped powermap
The values of the cropped powermap arrays are summed together
  If the total audio energy in the bounding box exceeds a set threshold the audio activity for that class is set to one, otherwise zero
  The new detections (with audio activity information and detection location in spherical coordinates) are outputted to a csv-file

## Slide 23: Output example
(a screenshot of output CSV file)

## Slide 24: Pipeline version 2

## Slide 25: Beamforming
Beamforming can also be used to determine audio activity (function by Archontis)
  ”Listens” to a pointed direction
  How to get a pointed direction?
    Multi-frame (video) audio segments
    Frame-level (video) audio segments
    DeepSORT

## Slide 26: Multi-frame (video) audio segments
We want to find the temporal trajectories of visual objects (from the video tracker)
Problem: how to find correspondences between objects in consecutive frames?
  Have only one object present in video (current implementation)
  Some more advanced method, e.g. a video object tracker
  Handle everything on frame-level (also implemented)

## Slide 27: Demo of only one object present in video

## Slide 28: Frame-level (video) audio segments
Basic idea:
  For each frame:
    Take the 100-ms audio segment corresponding to the video frame (video at 10 fps)
    List all detected objects within the frame
  For each object in a frame, give the bounding box center coordinates (azimuth, elevation) to the beamformer

## Slide 29: Demo of frame-level audio segments

## Slide 30: Future Development Targets

## Slide 31: Future Development
The project worked as a proof-of-concept
The system should be tested more vigorously
  More recordings, testing the produced data in actual training
  Trying out the system with a microphone array with a better spatial resolution
  Making the pipeline end-to-end
Adding more intelligent object tracking methods for producing accurate object trajectories within longer time windows (DeepSORT!)

## Slide 32: DeepSORT
DeepSort is a traditional single-hypothesis multi-target tracking method using recursive Kalman filtering and frame-by-frame data correlation.
DeepSort adopts the fusion metric that combining the distance of predicted position and the observed position in the Markov space and the cosine distance of the apparent feature between the bounding boxes in the Kalman filter.

## Slide 33: DeepSORT- Workflow
Figure : The workflow of real-time detection and tracking [1]

## Slide 34: DeepSORT – Object Detection
Input: {image, patches, image pyramid}
Backbone: {VGG16, ResNet50, ResNeXt-101, Darknet53}
Neck:
Head:
  Dense Prediction: {RPN, YOLO, SSD, Retina-Net, FCOS}
  Sparse Prediction: {Faster R-CNN, R-FCN} [2]
Figure : Architecture of object detection of YOLOv4 [2]

## Slide 35: DeepSORT – Kalman Filter
Source:https://www.codeproject.com/Articles/865935/Object-Tracking-Kalman-Filter-with-Ease

## Slide 36: Successes and Challenges
Overall the project proceeded quite steadily, no bigger obstacles all spring
At the very end we noticed that there was no licensing defined for the mp-YOLO github project we had used as a basis for the video detection part
  Contacted the developer and got a license file added! Phew.

## Slide 37: References
[1] Xu Zhang, Xiangyang Hao, Songlin Liu, Junqiang Wang, Jiwei Xu, Jun Hu, "Multi-target tracking of surveillance video with differential YOLO and DeepSort," Proc. SPIE 11179, Eleventh International Conference on Digital Image Processing (ICDIP 2019), 111792L (14 August 2019); doi: 10.1117/12.2540269
[2] Alexey Bochkovskiy,Chien-Yao Wang,Hong-Yuan Mark Liao, "YOLOv4: Optimal Speed and Accuracy of Object Detection ", 2020
[3] Wenyan Yang, Yanlin Qian, Francesco Cricri, Lixin Fan, Joni-Kristian Kamarainen, “Object Detection in Equirectangular Panorama”, 2018
[4] Tsung-Shan, Yang, mp-YOLO, https://github.com/keevin60907/mp-YOLO