## Slide 1: Automated spatiotemporal annotation of sound objects in a scene
Einari VAARAS
Kalle LAHTINEN
Mehmet AYDIN
COMP.SGN.250 Signal Processing Innovation Project
Final Presentation

## Slide 2: Introduction
Audio streams, such as broadcast news, documentaries and personal videos contain sounds from a wide variety of sound sources
These streams include detectable audio events of interest, such as speech, music or sounds of animals
Beside the detection of sound event presence there is a need for detecting the direction of arrival (DOA) of the detected sound event. For such cases Deep Learning methods are often used but requires annotated data which is laborious and difficult to do reliably
The aim is to explore the possibility of automatically annotating spatial and temporal dimensions of sound objects detected in an audio stream with the help of a 360-degree

## Slide 4: Project Steps
Studying object detection methods for 360-degree video data
Determining and defining the scenes to be recorded
Recording spatiotemporal scenes with a 360-degree camera and integrated 360-degree microphone
Applying object detection to the video recording
Extracting temporal object detections and their locations from the video recording
Formulating spatiotemporal labels for the audio data by combining video and audio detections

## Slide 5: Technologies
Ricoh Theta V 360 camera and TA-1 3D microphone module
  Microphone array of 4 microphones
YOLO (You Only Look Once) video detection network applied on 360 equirectangular video frames
  Method based on paper by Wenyan Yang, Yanlin Qian, Francesco Cricri, Lixin Fan, Joni-Kristian Kamarainen
  Open source github project found to use as a basis
B-format audio decoding, powermap calculation and beamforming scripts provided by Archontis Politis

## Slide 6: Implemented Pipelines
Pipeline version 1
Pipeline version 2

## Slide 7: Pipeline version 1

## Slide 8: Video Detector and Detection Output
YOLO video detection network
Equirectangular video frames projected to 4 sub image planes, which is fed to the detector
  So 4 YOLO detections per 360 frame

## Slide 9: Detection Output
Detections outputted to csv-file (frame id, class id, label, confidence, bounding box center coordinates, bounding box size)
All this is done offline, i.e. no hard time requirements for processing time

## Slide 10: Clean overlapping bounding boxes
Basic idea of algorithm:
  If there are same classes present in the same video frame:
    If there are overlapping bounding boxes (determined by IoU):
      If overlap exceeds a predetermined threshold:
        Remove bounding box with least confidence
Video demo

## Slide 11: Class mapping function
It is possible to change the class indeces and names of classes into arbitrary classes
Video demo

## Slide 12: Audio powermap
A function made by Archontis converts the B-format audio into a powermap
  MUSIC algorithm used
  (Some other details?)
Video demo

## Slide 13: Crop powermap using bounding boxes
The detectected bounding boxes in the frame are used to crop the powermap array
  Values within the bounding box are left unchanged, everything else is set to zero
Video demo

## Slide 14: Determine energy based on cropped powermap
The values of the cropped powermap arrays are summed together
  If the total audio energy in the bounding box exceeds a set threshold the audio activity for that class is set to one, otherwise zero
  The new detections (with audio activity information and detection location in spherical coordinates) are outputted to a csv-file
CSV file example

## Slide 15: Pipeline version 2

## Slide 16: Beamforming
Beamforming can also be used to determine audio activity
  ”Listens” to a pointed direction
  How to get a pointed direction?
    Multi-frame (video) audio segments
    Frame-level (video) audio segments
    DeepSORT

## Slide 17: Multi-frame (video) audio segments
We want to find the temporal trajectories of visual objects (from the video tracker)
Problem: how to find correspondences between objects in consecutive frames?
  Have only one object present in video (current implementation)
    File demo
  Some more advanced method, e.g. a video object tracker
  Handle everything on frame-level

## Slide 18: Frame-level (video) audio segments
Basic idea:
  For each frame:
    Take the 100-ms audio segment corresponding to the video frame (video at 10 fps)
    List all detected objects within the frame
  For each object in a frame, give the bounding box center coordinates (azimuth, elevation) to the beamformer
  File demo

## Slide 19: Future Development Targets

## Slide 20: Future Development
The project worked as a proof-of-concept
The system should be tested more vigorously
  More recordings, testing the produced data in actual training
  Trying out the system with a microphone array with a better spatial resolution
Adding more intelligent object tracking methods for producing accurate object trajectories within longer time windows (DeepSORT!)

## Slide 21: DeepSORT
DeepSort is a traditional single-hypothesis multi-target tracking method using recursive Kalman filtering and frame-by-frame data correlation.
DeepSort adopts the fusion metric that combining the distance of predicted position and the observed position in the Markov space and the cosine distance of the apparent feature between the bounding boxes in the Kalman filter.

## Slide 22: DeepSORT- Workflow
Figure : The workflow of real-time detection and tracking [1]

## Slide 23: DeepSORT – Object Detection
Input: {image, patches, image pyramid}
Backbone: {VGG16, ResNet50, ResNeXt-101, Darknet53}
Neck:
Head:
  Dense Prediction: {RPN, YOLO, SSD, Retina-Net, FCOS}
  Sparse Prediction: {Faster R-CNN, R-FCN} [2]
Figure : Architecture of object detection of YOLOv4 [2]

## Slide 24: DeepSORT – Kalman Filter
Source:https://www.codeproject.com/Articles/865935/Object-Tracking-Kalman-Filter-with-Ease

## Slide 25: Successes and Challenges
Overall the project proceeded quite steadily, no bigger obstacles all spring
At the very end we noticed that there was no licensing defined for the mp-YOLO github project we had used as a basis for the video detection part
  Contacted the developer and got a license file added! Phew.

## Slide 26: References
[1] Xu Zhang, Xiangyang Hao, Songlin Liu, Junqiang Wang, Jiwei Xu, Jun Hu, "Multi-target tracking of surveillance video with differential YOLO and DeepSort," Proc. SPIE 11179, Eleventh International Conference on Digital Image Processing (ICDIP 2019), 111792L (14 August 2019); doi: 10.1117/12.2540269
[2] Alexey Bochkovskiy,Chien-Yao Wang,Hong-Yuan Mark Liao, "YOLOv4: Optimal Speed and Accuracy of Object Detection ", 2020
[3] Wenyan Yang, Yanlin Qian, Francesco Cricri, Lixin Fan, Joni-Kristian Kamarainen, “Object Detection in Equirectangular Panorama”, 2018
[4] Tsung-Shan, Yang, mp-YOLO, https://github.com/keevin60907/mp-YOLO